## Slide 1
IMAGE PROCESSING USING PYTHON
for
III B.Tech (CSM & AIML) - I Semester
By
T. Vijaya Kumar
Assistant Professor
Dept. of ECE, VVIT

## Slide 2
UNIT – II
IMAGE ENHANCEMENT

## Slide 3
UNIT – II Image Enhancement
Spatial domain methods:
  Point & Histogram processing
  Fundamentals of Spatial filtering
  Smoothing spatial filters
  Sharpening spatial filters
Frequency domain methods:
  Basics of filtering in frequency domain
  Image smoothing
  Image sharpening
  Selective filtering
SYLLABUS
Text Books:
Digital Image Processing – Gonzaleze and Woods, 2nd Ed., Pearson.
S. Jayaraman, S. Esakkirajan and T. VeeraKumar, “Digital Image processing, Tata McGraw Hill publishers, 2009

## Slide 4
UNIT – II: Image Enhancement in the Spatial Domain
Spatial domain methods
Point Processing
Histogram processing
Fundamentals of Spatial filtering
Smoothing Spatial filters
Sharpening spatial filters
Combining spatial enhancement methods

## Slide 5
UNIT – II: Image Enhancement in the Spatial Domain
Introduction
Spatial domain
Image plane itself, directly process the intensity values of the image plane.
Transform domain
process the transform coefficients, not directly process the intensity values of the image plane.

## Slide 6
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 7
UNIT – II: Image Enhancement in the Spatial Domain
Contd…
A 3*3 neighborhood about
a point (x, y) in an image

## Slide 8
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 9
UNIT – II: Image Enhancement in the Spatial Domain
Point Processing
Image Negatives
Log Transformations
Power-Law Transformations
Piecewise-Linear Transformation Functions
    Thresholding
    Contrast Stretching
    Intensity-level slicing
        Gray-level slicing
        Bit-plane slicing

## Slide 10
UNIT – II: Image Enhancement in the Spatial Domain
Contd…
Fig. Some basic gray-level transformation functions used for image enhancement

## Slide 11
UNIT – II: Image Enhancement in the Spatial Domain
Image Negatives

## Slide 12
UNIT – II: Image Enhancement in the Spatial Domain
Example: Image Negatives
Small lesion

## Slide 13
UNIT – II: Image Enhancement in the Spatial Domain
Log Transformations

## Slide 14
UNIT – II: Image Enhancement in the Spatial Domain
Example: Log Transformations

## Slide 15
UNIT – II: Image Enhancement in the Spatial Domain
Power-Law Transformations
Plots of the equation
s = c rγ for various
values of γ (c=1 in all cases)

## Slide 16
UNIT – II: Image Enhancement in the Spatial Domain
Example: Gamma Transformations

## Slide 17
UNIT – II: Image Enhancement in the Spatial Domain
Example: Gamma Transformations

## Slide 18
Contrast Stretching
— Expands the range of intensity levels in an image so that it spans the full intensity range of the recording medium or display device.
Intensity-level Slicing
— Highlighting a specific range of intensities in an image often is of interest.
UNIT – II: Image Enhancement in the Spatial Domain
Piecewise-Linear Transformations

## Slide 19
UNIT – II: Image Enhancement in the Spatial Domain
Contrast Stretching

## Slide 20
UNIT – II: Image Enhancement in the Spatial Domain
Gray-level slicing

## Slide 21
UNIT – II: Image Enhancement in the Spatial Domain
Example: Gray-level slicing

## Slide 22
UNIT – II: Image Enhancement in the Spatial Domain
Bit-plane Slicing

## Slide 23
UNIT – II: Image Enhancement in the Spatial Domain
Example: Bit-plane slicing

## Slide 24
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 25
UNIT – II: Image Enhancement in the Spatial Domain
Example: Bit-plane slicing
An 8-bit fractal image

## Slide 26
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 27
Histogram Equalization
Histogram Matching
Local Histogram Processing
UNIT – II: Image Enhancement in the Spatial Domain
Histogram Processing

## Slide 28
UNIT – II: Image Enhancement in the Spatial Domain
Introduction

## Slide 33
UNIT – II: Image Enhancement in the Spatial Domain
Histogram Equalization
It is a process that attempts to spread out the gray levels in an image so that they are evenly distributed across their image
Procedure to perform Histogram Equalization
Find the running sum of the histogram values.
Normalize the values from step (1) by dividing by the total number of pixels.
Multiply the values from step (2) by the maximum gray level value and round.
Map the gray level values to the results from step (3) using a one-to-one correspondence.

## Slide 34
UNIT – II: Image Enhancement in the Spatial Domain
Example: Histogram Equalization
Q. Suppose that a 3-bit image (L=8) of size 5 × 5 pixels has the intensity distribution shown in following table. Perform histogram equalization of the image ?
rk | nk
0 | 0
1 | 0
2 | 0
3 | 6
4 | 14
5 | 5
6 | 0
7 | 0
4 4 4 4 4
3 4 5 4 3
3 5 5 5 3
3 4 5 4 3
4 4 4 4 4

## Slide 35
Gray level | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Number of pixels | 0 | 0 | 0 | 6 | 14 | 5 | 0 | 0
Running sum | 0 | 0 | 0 | 6 | 20 | 25 | 25 | 25
Running sum / Total number of pixels | 0/25 | 0/25 | 0/25 | 6/25 | 20/25 | 25/25 | 25/25 | 25/25
Multiply the above result by maximum gray level | (0/25)*7 = 0 | (0/25) *7 = 0 | (0/25) *7 = 0 | (6/25) *7 = 2 | (20/25) *7 = 6 | (25/25) *7 = 7 | (25/25) *7 = 7 | (25/25) *7 = 7
Example: Histogram Equalization

## Slide 36
UNIT – II: Image Enhancement in the Spatial Domain
Mapping of gray level by a one-to-one correspondence
Original gray level | Histogram equalized values
0 | 0
1 | 0
2 | 0
3 | 2
4 | 6
5 | 7
6 | 7
7 | 7
Example: Histogram Equalization

## Slide 37
UNIT – II: Image Enhancement in the Spatial Domain
4 4 4 4 4
3 4 5 4 3
3 5 5 5 3
3 4 5 4 3
4 4 4 4 4
Histogram
Equalization
6 6 6 6 6
2 6 7 6 2
2 7 7 7 2
2 6 7 6 2
6 6 6 6 6
Example: Histogram Equalization

## Slide 38
Q. Suppose that a 3-bit image (L=8) of size 64 × 64 pixels (MN = 4096) has the intensity distribution shown in following table. Get the histogram equalization transformation function and give the ps(sk) for each sk.
UNIT – II: Image Enhancement in the Spatial Domain
Example: Histogram Equalization

## Slide 39
Example: Histogram Equalization

## Slide 40
UNIT – II: Image Enhancement in the Spatial Domain
Example: Histogram Equalization

## Slide 42
Example: Histogram Equalization

## Slide 43
— generate a processed image that has a specified histogram
Development of the method
Determine the transformation ( sk ) = T ( rk ) that can equalize the original image's histogram pr(r).
2. Determine the transformation (sk ) = G ( bk ) that can equalize the desired image's histogram pb(b).
3. Perform transformation G-1(T(rk )) .
UNIT – II: Image Enhancement in the Spatial Domain
Histogram Matching (Specification)

## Slide 44
Q. Suppose that a 3-bit image (L=8) of size 64 × 64 pixels (MN = 4096) has the intensity distribution shown in the following table (on the left). Get the histogram transformation function and make the output image with the specified histogram, listed in the table on the right.
UNIT – II: Image Enhancement in the Spatial Domain
Example: Histogram Matching

## Slide 45
Obtain the scaled histogram-equalized values,
Compute all the values of the transformation function G,

## Slide 46
Obtain the scaled histogram-equalized values,
Compute all the values of the transformation function G,
s0
s2
s3
s5
s6
s7
s1
s4

## Slide 50
- Define a neighborhood and move its center from pixel to pixel
- At each location, the histogram of the points in the neighborhood is computed. Either histogram equalization or histogram specification transformation function is obtained
- Map the intensity of the pixel centered in the neighborhood
- Move to the next location and repeat the procedure
UNIT – II: Image Enhancement in the Spatial Domain
Local Histogram Processing

## Slide 51
UNIT – II: Image Enhancement in the Spatial Domain
Example: Local Histogram Processing

## Slide 52
- A spatial filter consists of (a) a neighborhood, and (b) a predefined operation
- Linear spatial filtering of an image of size MxN with a filter of size mxn is
given by the expression
UNIT – II: Image Enhancement in the Spatial Domain
Fundamentals of Spatial Filtering

## Slide 53
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 54
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 55
- Smoothing filters are used for blurring and for noise reduction
- Blurring is used in removal of small details and bridging of small gaps in lines or curves
- Smoothing spatial filters include
    Linear filters
      Averaging Filter
    Nonlinear filters
      Median Filter
      Maximum Filter
      Minimum Filter
UNIT – II: Image Enhancement in the Spatial Domain
Smoothing Spatial Filters

## Slide 56
UNIT – II: Image Enhancement in the Spatial Domain
Spatial Smoothing Linear Filters

## Slide 57
UNIT – II: Image Enhancement in the Spatial Domain
Smoothing Averaging Filter Masks

## Slide 58
UNIT – II: Image Enhancement in the Spatial Domain
Example: Smoothing Averaging Filter Masks

## Slide 59
UNIT – II: Image Enhancement in the Spatial Domain
Example: Smoothing Averaging Filter Masks

## Slide 60
— Nonlinear
— Based on ordering (ranking) the pixels contained in the filter mask
— Replacing the value of the center pixel with the value determined by the ranking
result
E.g., Median filter
Max filter
Min filter
UNIT – II: Image Enhancement in the Spatial Domain
Order-statistic (Nonlinear) Filters

## Slide 61
UNIT – II: Image Enhancement in the Spatial Domain
Example: Use of Median Filtering for Noise Reduction

## Slide 62
UNIT – II: Image Enhancement in the Spatial Domain
Sharpening Spatial Filters

## Slide 63
Foundation
Laplacian Operator
Unsharp Masking and High boost Filtering
Using First-Order Derivatives for Nonlinear Image Sharpening — The Gradient
UNIT – II: Image Enhancement in the Spatial Domain
Sharpening Spatial Filters

## Slide 64
The first-order derivative of a one-dimensional function f(x) is the difference
The second-order derivative of f(x) as the difference
UNIT – II: Image Enhancement in the Spatial Domain
Foundation of sharpening filters

## Slide 65
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 66
- The second-order isotropic derivative operator is the Laplacian for a function (image) f(x,y)
UNIT – II: Image Enhancement in the Spatial Domain
Laplacian Operator

## Slide 67
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 68
Image sharpening in the way of using the Laplacian
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 69
UNIT – II: Image Enhancement in the Spatial Domain
Example: Laplacian Operator

## Slide 70
Unsharp masking
- Sharpen images consists of subtracting an unsharp (smoothed) version of an
image from the original image
e.g., printing and publishing industry
Steps
1. Blur the original image
2. Subtract the blurred image from the original
3. Add the mask to the original
UNIT – II: Image Enhancement in the Spatial Domain
Unsharp Masking & High boost Filtering

## Slide 71
UNIT – II: Image Enhancement in the Spatial Domain
Unsharp Masking & High boost Filtering

## Slide 72
UNIT – II: Image Enhancement in the Spatial Domain
Example: Unsharp Masking and High boost Filtering

## Slide 73
Gradient Image
UNIT – II: Image Enhancement in the Spatial Domain
Gradient (First-Order Derivatives)

## Slide 74
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 75
z1 | z2 | z3
z4 | z5 | z6
z7 | z8 | z9
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 76
UNIT – II: Image Enhancement in the Spatial Domain
Contd…

## Slide 77
UNIT – II: Image Enhancement in the Spatial Domain

## Slide 78
UNIT – II: Image Enhancement in the Spatial Domain
Example: Sobel Operator

## Slide 79
UNIT – II: Image Enhancement in the Spatial Domain
Example: Sobel Operator